## Slide 1: trackopt - Update
Jannis Maron
Universität Siegen

## Slide 2: Applications
Rigid Body Motion
Elastic Deformation
Holographic Particles
Source: Prof. Jari Hyttinen, Tampere University
Source: anvajo - fludlab-r300

## Slide 3: Rigid Body Motion
We Observed:
Phase-Video of a rotating transparent HEK Cell.
Problem:
Geometry of the cell.
Pose for any given frame.
  Translation
  Rotation
What to do?
Work with some initial assumptions.
Simulate the scattering of the wavefield.
Then optimize geometry/poses to fit the video sequence.
Observed Phase of a rotating HEK Cell
The Goal:
Reconstruct the Refractive Index (RI) distribution of the cell as a 3D Volume.
⇒ RI-Tomography
We don’t know:

## Slide 4
Recap: Last time
Simulate scattering of a wavefield through an RI Distribution, where we are in control of:
Geometry
Position
Rotation
Based on a non-scattering tomography with sensible poses.
Estimated Initial RI Distribution:
Wavefield Simulation:
Fixed position/rotation axis
Constant angular velocity

## Slide 5
Recap: Forward Simulation
Optimize the pose to obtain a better guess for the RI Distribution.
Next:
Notes: TODO:
- Redo Video with Clean GT DHM Data

## Slide 6: Single Frame Optimization
Domain Adaptations:
Objective/Loss Function
Optimization
Update pose parameters using gradient descent, comparing the simulated wavefield to the real wavefield.
Increase similarities between the ground truth and the simulated wavefield using different transforms:
Upscaling/Cropping
Gaussian Blur
Normalization
Compute Loss by comparing the Mean Squared Error and Normalized Cross-Entropy of simulated amplitude and phase to their ground truth counterparts.
Notes: Create Animation

## Slide 7: Single Frame Optimization
Domain Adaptations:
Objective/Loss Function
Optimization
Update pose parameters using gradient descent, comparing the simulated wavefield to the real wavefield.
Increase similarities between the ground truth and the simulated wavefield using different transforms:
Upscaling/Cropping
Gaussian Blur
Normalization
Compute Loss by comparing the Mean Squared Error and Normalized Cross-Entropy of simulated amplitude and phase to their ground truth counterparts.
Notes: Create Animation

## Slide 8: Single Frame Optimization
Success!
We can find a pose such that our simulated wavefield resembles the real wavefield.
What now?
Optimize the whole video sequence!

## Slide 9: Frame-by-Frame Pose Optimization
Next Frame:
Regularization:
Initialize the next frame with the best pose of the previous frame.
Add an additional Regularization Loss to our previous Data Loss to encourage a smooth pose trajectory.
L2 Distance between subsequent Positions
Kalman Filter predictions for subsequent Rotations
Notes: Create Animation

## Slide 10: Frame-by-Frame Pose Optimization
Next Frame:
Regularization:
Initialize the next frame with the best pose of the previous frame.
Add an additional Regularization Loss to our previous Data Loss to encourage a smooth pose trajectory.
L2 Distance between subsequent Positions
Kalman Filter predictions for subsequent Rotations
Notes: Create Animation

## Slide 11: Frame-by-Frame Pose Optimization

## Slide 12: Reconstruction Optimization
Problem:
We were unable to utilize the improved pose estimates to apply non-scattering RI-Tomography and obtain a better RI Distribution.
Solution:
⇒ Use our Simulation!
Rather than updating the poses, update the 3D volume.
Reconstruction Optimization:
Run the simulation for every optimized pose/frame and accumulate gradients. Update the 3D Volume once we have passed every pose.
Reconstruction Regularization:
Use a TV Regularization to encourage a smooth 3D volume.

## Slide 13: Inverse Simulation Tomography
⇒ End-to-End Optimization
Perform Pose Optimization to get updated poses.
Update Volume with the Reconstruction Optimization using the updated poses.
Repeat with updated RI. Distribution and pose of the first frame.
Initialization:
Estimated RI Distribution
Guessed Pose for first frame
Combined Optimization:
Update Domain Adaptations:
Reduce Gaussian blur every full loop.

## Slide 14: Inverse Simulation Tomography

## Slide 15: Current State of things
We aren’t the first to do this!
Moser et al.: Optical tomography reconstructing 3D motion and structure of multi-scattering samples under rotational actuation
So far, we haven’t been able to reproduce their method successfully.
Problem:

## Slide 16: The Future
Soon:
New Tasks, new challenges.
And then?
Elastic Deformation
Holographic Particles
Novelty to Moser et al. and publish results.
Extend to new data (Coded WFS)
Technical ablation (What does work, what doesn’t)
Incremental improvements

## Slide 17
Thank you!
Jannis.Maron@uni-siegen.de